## Slide 1: Understanding the Roadside Environment through Integrating Air Quality & Traffic-Related Data
Christine Kendrick

## Slide 3: Roadside Data Collection

## Slide 4: Roadside Data Collection
Continuous monitoring:
  Teledyne T200 NO, NO2, NOx chemiluminescence analyzer
  TSI DustTrak DRX PM2.5
  Wind speed & direction
  Temperature & relative humidity
Urban background data:
  NO, NO2, aerosols, meteorology
Sydney Coordinated Adaptive Traffic Signal System (SCATS)
  traffic volumes
  cycle lengths
  green time, red time

## Slide 5: Pollutants vs Traffic Volumes
NOx (ppb)
PM2.5 (µg/m3)
Traffic Volumes (veh/15 mins)

## Slide 6: Seasonal Dirunal Patterns

## Slide 7: Findings- Annual Scale

## Slide 8: Findings
Morning periods across all seasons show significant linear relationship while evening periods do not
However, variability is high
Traffic volumes are not a good proxy at short-term time aggregations
Notes: Mention random sampling method to deal with temporal autocorrelation

## Slide 9: Findings
Season | Time Period | Coefficient NO per 100 vehicles per 15 mins | Standard Error of Coefficient NO per 100 vehicles per 15 mins | Adjusted r2 | Coefficient NO2 per 100 vehicles per 15 mins | Standard Error of Coefficient NO2 per 100 vehicle per 15 mins | Adjusted r2
Fall | Morning | 6.3 ** (7.9)** | 1.4 (0.4) | 0.1 (0.16) | 1.2** (1.6)** | 2.3 (0.1) | 0.14 (0.24)
Winter | Morning | 9.4** (11.2)** | 1.4 (0.7) | 0.14 (0.24) | 1.5** (1.9)** | 0.4 (0.2) | 0.17 (0.26)
Spring | Morning | 6.3** (6.7)** | 0.8 (0.3) | 0.41 (0.43) | 2.5** (2.3)** | 0.3 (0.2) | 0.27 (0.28)
Summer | Morning | 4.6** (4.4)** | (0.4) (0.2) | (0.45) (0.37) | 1.3** (1.6)** | 0.3 (0.1) | 0.25 (0.23)
Fall | Evening | -1.3 (-1.6) | 2.5 (1.1) | <0.001 (0.005) | 1.2* (0.9) | 0.6 (0.2) | 0.05 (0.03)
Winter | Evening | -0.04 (0.09) | 2.6 (1.3) | 0.002 (0.001) | -0.4 (-0.08) | 0.8 (0.4) | 0.05 (0.03)
Spring | Evening | 2.1 (2.2)** | 1.1 (0.5) | 0.03 (0.04) | 0.9 (0.9)** | (0.8) (0.3) | 0.007 (0.02)
Summer | Evening | 2.1* (2.9)** | 0.8 (0.3) | 0.02 (0.07) | 1.6* (1.9)** | 0.7 (0.2) | 0.03 (0.05)

## Slide 10: Implications of Findings
Morning time periods are more consistent input throughout the year for modeling transportation and air quality impacts
Other measures besides PM2.5 mass may be needed at certain locations to capture the increased particulate exposure from traffic
As exposure assessment moves toward predicting exposures on shorter time scales, traffic volumes as a proxy is not a reliable method
  Modeling based on evening periods when traffic volumes are higher could be overestimating or underestimating exposure concentrations

## Slide 11: Questions?
Christine.Kendrick@portlandoregon.gov

## Slide 12: Extra slides

## Slide 13
Findings